## Slide 1
Dr. P. Vijayalakshmi Professor, Department of ECE SSNCE
Reference : Digital Image processing – Rafael Gonzalez, Richard E. Woods
Histogram equalization & specification

## Slide 2: Histogram processing
Histogram: of a digital image with gray levels 0 to L-1 is a
discrete function of h(rk) = nk
rk – kth gray level
nk – number of pixels having gray levels rk
Normalized histogram p(rk) = nk/n
n – total number of pixels in the image
Normalized histogram gives an estimate of probability of occurrence of each gray level. Sum of all the components in an normalized histogram is 1.
Useful in compression, segmentation

## Slide 3: Image and histogram
Courtesy: Gonzalez & woods, Digital image processing

## Slide 4: Image and histogram
1600
1400
1200
1000
800
600
400
200
0
0
50
100
150
200
250
Histogram equalization
Histogram matching or histogram specification

## Slide 5: Histogram equalization
Histogram equalization:
To transform the gray levels of the image so that the histogram of the resultant image has histogram equalized or uniformly distributed.
Used for modifying the contrast
To equally make use of all the available gray levels in the dynamic range
To further process it for histogram matching or specification

## Slide 6
Assuming the pixel values are continuous functions
p(s) ds = p(r) dr
That is probability density of the transformed variable ‘s’
is determined by the gray level distribution of the input
image and by the chosen transformation function s = T(r)

## Slide 7: Histogram equalization
Steps involved:
  Find the number of pixels in each gray level and total number
of pixels
  Find the probability mass function of all the pixels in the image
  Find the cumulative distribution function
  Multiply the cumulative distribution function by L-1, L being the maximum gray level, to obtain new gray levels
  Map the new gray level values to the pixels with old gray levels.

## Slide 8: Histogram equalization
Mapping each pixel with level rk in the input image into
the corresponding pixel with level sk in the output image
Gray level values | Number of pixels | Probability mass function | Cumulative distribution function
0 | 790 | 0.19 | 0.19
1 | 1023 | 0.25 | 0.44
2 | 850 | 0.21 | 0.65
3 | 656 | 0.16 | 0.81
4 | 329 | 0.08 | 0.89
5 | 245 | 0.06 | 0.95
6 | 122 | 0.03 | 0.98
7 | 81 | 0.02 | 1.00

## Slide 9: Histogram equalization
Gray level values | Number of pixels | Probability mass function | Cumulative distribution function | CDF * L-1
0 | 790 | 0.19 | 0.19 | 1.33 = 1
1 | 1023 | 0.25 | 0.44 | 3.08 = 3
2 | 850 | 0.21 | 0.65 | 4.55 = 5
3 | 656 | 0.16 | 0.81 | 5.67 = 6
4 | 329 | 0.08 | 0.89 | 6.23 = 6
5 | 245 | 0.06 | 0.95 | 6.65 = 7
6 | 122 | 0.03 | 0.98 | 6.86 = 7
7 | 81 | 0.02 | 1.00 | 7 = 7

## Slide 10: Distributions (PMF, CDF)
2
4
6
8
0
0
0.4
0.2
2
4
6
8
0
0
1
0.5
2
4
6
8
0
0
1
0.5

## Slide 11: Mapping
Mapping:
Old gray level values | New gray level values | Frequency of occurrence
0 | 1 | 790
1 | 3 | 1023
2 | 5 | 850
3 | 6 | 656
4 | 6 | 329
5 | 7 | 245
6 | 7 | 122
7 | 7 | 81

## Slide 12: Histogram equalization
1600
1400
1200
1000
800
600
400
200
0
0
50
100
150
200
250

## Slide 13: Histogram matching or specification
Specify the shape of the histogram we wish the processed
image should have
The method used to generate a processed image that has a specified histogram is called histogram matching or histogram specification
Steps involved:
  Equalize the histogram of the input image
  Equalize the specified histogram
  Relate the two equalized histograms

## Slide 14: Histogram matching

## Slide 15
Matching


## Slide 16: Example

## Slide 17: Example
Gray level values | Number of pixels | Probability mass function | Cumulative distribution function
0 | 790 | 0.19 | 0.19
1 | 1023 | 0.25 | 0.44
2 | 850 | 0.21 | 0.65
3 | 656 | 0.16 | 0.81
4 | 329 | 0.08 | 0.89
5 | 245 | 0.06 | 0.95
6 | 122 | 0.03 | 0.98
7 | 81 | 0.02 | 1.00
Gray level values | Probability mass function | Cumulative distribution function
0 | 0 | 0
1 | 0 | 0
2 | 0 | 0
3 | 0.15 | 0.15
4 | 0.2 | 0.35
5 | 0.3 | 0.65
6 | 0.2 | 0.85
7 | 0.15 | 1.0

## Slide 18: Example
Input gray level | Cumulative distribution function | Cumulative distribution function | Output gray level
0 | 0.19 | 0.0 | 3
1 | 0.44 | 0.0 | 4
2 | 0.65 | 0.0 | 5
3 | 0.81 | 0.15 | 6
4 | 0.89 | 0.35 | 6
5 | 0.95 | 0.65 | 7
6 | 0.98 | 0.85 | 7
7 | 1.0 | 1.0 | 7
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
j | 3 | 4 | 5 | 6 | 6 | 7 | 7 | 7